## Slide 1: COSMIC ACCESS Workshop Lab: Inter-center Demonstration
Presented by:
Stephen Leroy
Atmospheric and Environmental Research
Lexington, MA
August 16, 2023

## Slide 2: Organization
Google “aws radio occultation”
  GitHub site contains documentation and tutorial demonstration notebooks
  “Browse Bucket” shows the structure of the repository
contributed/v1.1/center/mission/filetype/year/month/day/*.nc
File types
  calibratedPhase is level 1b, including precise orbits, excess phase, amplitude data
  refractivityRetrieval is level 2a, containing retrieved bending angle vs. impact parameter and retrieved refractivity vs. altitude/height.
  atmosphericRetrieval is level 2b, containing retrieved pressure, temperature, and water vapor vs. height.
Occultation identification: receiver-transmitter-time
  Receivers are defined in GitHub documentation and can be discovered by query
  Transmitters are RINEX standard, e.g. “G03”. Constellations: G = GPS, R = GLONASS, E = Galileo, C = BeiDou. A PRN (“03”) identifies a satellite according to the signals it broadcasts.
  Time

## Slide 3: Organization
AWS command line interface (“awscli”) allows for high bandwidth download of data directly from bucket
aws s3 sync s3://gnss-ro-data/contributed/v1.1/ucar/cosmic2/refractivityRetrieval/2022/03/20/ ./
--no-sign-request
Database contents: one JSON file per mission per day
dynamo/v1.1/export_subsets/*.json
Mirror the entire database in advance
mkdir –p ~/rodatabase
aws s3 sync s3://gnss-ro-data/dynamo/v1.1/export_subsets/ ~/rodatabase/ --no-sign-request

## Slide 4: API: Key elements
Objects
  RODatabaseClient
  OccList
Query options
  datetimerange: tuple( ISO-format-time, ISO-format-time ): “2008-03-05T12:37:00”, for example
  missions: a string or list of strings or a tuple of strings
  availablefiletypes: a string or a list of strings or a tuple of strings. “{center}_{filetype}” where center is “ucar”, “romsaf”, or “eumetsat” and filetype is “calibratedPhase”, “refractivityRetrieval”, or “atmosphericRetrieval”
File types
  calibratedPhase is level 1b, including precise orbits, excess phase, amplitude data
  refractivityRetrieval is level 2a, containing retrieved bending angle vs. impact parameter and retrieved refractivity vs. altitude/height.
  atmosphericRetrieval is level 2b, containing retrieved pressure, temperature, and water vapor vs. height.
Info options: “mission”, “receiver”, “transmitter”, “datetime”, “localtime”, “longitude”, “latitude”, “geometry”, “filetype”
Values options: ”longitude”, “latitude”, ”localtime”, “datetime”, “{center}_{filetype}”

## Slide 5: GitHub support, tutorials, etc.
On your EC2 instance…
git clone https://github.com/gnss-ro/aws-opendata.git

## Slide 6: Jupyter notebook structure
Geolocation demonstration
Imports
Database
  Instantiate database client
  Query the database
Data analysis
  Get metadata (“values”)
Plot results
  matplotlib.pyplot.Axes, cartopy.crs
  Subset the OccList according to mission/geometry/etc.
  Show output (plt.show()) or save figure (plt.savefig(…))
Inter-center comparison demonstration
Imports
Database
  Instantiate database client
  Query the database
  Subset the OccList according to mission/geometry/etc.
  Download data
Data analysis
  Loop over downloaded data
  Interpolate profiles
  Perform statistics
  Save findings to file, JSON or NetCDF
Plot results
  Read results of data analysis from save file
  matplotlib.pyplot.Axes, cartopy.crs
  Show output (plt.show()) or save figure (plt.savefig(…))

## Slide 7: Assignment
Plot occultation distributions on a map and in local time
Color-code by mission
Try different epochs
Distribution of planetiq occultations, by GNSS constellation
Center inter-comparison for bending angles
Global
Subset statistics by latitude bins
Center inter-comparison for occultation penetration depth
In Tropics, how deep to occultations penetrate?
Directly compare two centers

## Slide 8: Time for lab…
For more information, please contact
Stephen Leroy
Principal Scientist
sleroy@aer.com
+1 (781) 761-2234